## Slide 1: Zenith35/ Pro «TAG SINGLE MODE»

## Slide 2: Contents
  Required Equipment
  TAG Single Mode – what is it?
  TAG Single Mode – Typical accuracy
  Compass Calibration
  Examples & Recommendations

## Slide 3: Required Equipment
  Zenith35 TAG or Zenith35 Pro TAG
  Latest onboard firmware version installed
        Zenith35 TAG ≥ V 1.25
        Zenith35 Pro TAG ≥ V 2.01
  Compass Calibration Tool
  Latest Field Software version installed
    X-PAD ≥ V 3
    GeoMax FieldGenius ≥ V 9
  Field Controller
  GNSS Pole

## Slide 4: What is the «TAG-Single»
      Zenith35 TAG includes tilt sensors for pole tilt calculation and e-compass to detremine the North direction
      All Zenith35/Pro TAG includes tilt sensors and compass
      Until now Zenith35 TAG was available only with «TAG-Dual mode»
      Hidden points was measured with two measures with pole was tilted

## Slide 5: What is the «TAG-Single»
      The last firmware enables the electronic compass installed within the Zenith35/ Pro TAG
      The new firmware enables the e-compass to estimate the North direction
      This allows you to measure points without holding the pole levelled and vertical
      Only one measure is needed to record points with the pole tilted

## Slide 6: What is the «TAG-Single»
      1 point measurements  to increase efficiency
      Suitable for survey and stakeout operations!
      Tilt range: 15°
       equals to 52cm deflection @2m pole height

## Slide 7: What is the «TAG-Single»
      The Tilt Sensor is used to determine the degree of inclination. This is measured with accelerometers
      The Compass is used to determine the direction of tilt. This is measured by magnetometers
       Since the compass principle is based on the earth magnetic field, measuring with the compass close to metal objects with an own magnetic field or objects generating magnetic fields such as generators is error-prone.

## Slide 8: Accuracy
 | 2D- Position** | 1D-Position (Height)
5°-Tilt | ~ ±1 cm | ~ ±1 cm
10°-Tilt | ~ ±2 cm | ~ ±1.2 cm
15°-Tilt | ~ ±3 cm | ~ ±1.5 cm
    Accuracy (typical)*
* The following values represent an average achieved during tests under normal to favourable conditions.
** Please note that these error needs to be applied on top of the standard GNSS accuracy.

## Slide 9: Compass calibration
      Before starting to use the compass it is needed to perform a calibration routine
      The calibration rountine has 3 main steps:
        Calibrate the e-bubble
        Scanning modelling the local magnetic field
        Controlling if the calculated model fist
      A calibration tool is needed to perform the calibration
        Included in new Zenith35 Pro TAG packages or as an optional accessory for Zenith35 TAG

## Slide 10: Compass calibration – Local conditions
      The compass is sensible to magnetic fields, such as
        Local earth’s magnetic field
        Cars
        Powerlines
        Generators
        Steel reinforced buildings
        Choose a location where the possible interferences are minimum
        Calibration of the compass is required to “fit” the local earth’s magnetic field, conditions, surroundings and environment. The calibration must be done before starting the measurement campaign

## Slide 11: Compass calibration – X-PAD
      To start the calibration routine open the X-PAD instrument settings
      Create a new profile or modify an existing profile
      In the Antenna page click on Compass to start the calibration routine

## Slide 12: Compass calibration – FieldGenius
      To start the calibration routine after the Zenith35/ Pro is configured and connected open Instrument Settings and Sensor Configure
      Click on Electronic Bubble
      Click on Calibration to start the calibration routine

## Slide 13: Compass calibration
      To calibration is done in different steps
      IMPORTANT: The receiver must be fixed while doing the calibration routine!

## Slide 14: Compass calibration
      Click on Communication to verify that the Zenith35/Pro TAG is connected by Bluetooth

## Slide 15: Compass calibration
      Click on E-bubble to start to calibrate the electronic bubble
      You must stay vertical with the pole and press START

## Slide 16: Compass calibration
      Check that the result is correct
      Press Accept to validate the result

## Slide 17: Compass calibration
      Click on Compass to open the next step
      Mount the calibration tool on the pole

## Slide 18: Compass calibration
      Click Start and slowly rotate clockwise the pole, while vertical
      The full rotation should take about 40-60 seconds

## Slide 19: Compass calibration
      If the calibration is well done you see a circle. After the progress bar is completed, click Continue
      If on the left side you don’t see a circle, but the points are random, it is recommended to change the calibration area

## Slide 20: Compass calibration
      Unmount the calibration tool and place the pole vertical
      As before rotate clockwise the pole within 40-60 seconds

## Slide 21: Compass calibration
      If the calibration is well done you see a circle. After the progress bar is completed, click Continue

## Slide 22: Compass calibration
      For the next step verify that the receiver is FIXED
      Occupy a marked ground position and click Start to measure the point. When done press Continue.

## Slide 23: Compass calibration
      While on the same marker, you must measure 4 points with the pole tilted and oriented on different Azimuth angles
      You must tilt the pole until the Diff.Tilt value is close to zero and rotate around the point until the Diff Azimuth is close to zero

## Slide 24: Compass calibration
      While the two angles are close to zero the instrument measures the point
      Wait few seconds until point is saved. Then rotate to next angle

## Slide 25: Compass calibration
      Proceed in the same way for all the four points
      When done press Continue to complete the calibration

## Slide 26: Compass calibration
      Enter the pole height
      Check that the calibration is succesful!

## Slide 27: Compass calibration
      Calibration is done and now you can start to use the compass to measure all points with pole tilted!
      GeoMax FieldGenius
        Enable it from Electronic Bubble menu

## Slide 28: Compass calibration
      X-PAD
        Enable it from Survey Settings

## Slide 29: When re-calibrate?
      A re-calibration is needed after:
        A change of location
        A significant drop
        A significant temperature change (30° or more)
        A long period without calibration
        A transport (-> vibration)
        A battery is inserted that was never inseted before
        A firmware upgrade
       Not calibrating the unit after events as listed above negatively affects the accuracy of the measured points.

## Slide 30: Examples and Recommendations
Bad measurement conditions - Following examples showing locations with high magnetic influence, resulting in a point accuracy about 5-10 times worse as typical. Typical situations are measurement close to cars, lamp poles, and power lines. Errors of 30-50 cm appeared during our tests….
 In those cases it is mandatory either to switch off the Single mode at all and measure in conventional way, holding the pole vertical or if not possible, to use the dual mode to eliminate the magnetic influence.

## Slide 31: Examples and Recommendations
Medium measurement conditions - Following examples showing locations with some magnetic influence, resulting in point accuracy worse as typical. Typical situations are measurement on car-parking lots, house corners, close to metal fences….
 In such conditions, it is strongly recommended to perform a control measurement to see if the achieved accuracy is sufficient.

## Slide 32: Examples and Recommendations
Good measurement conditions - Following examples showing locations with low to none magnetic influence, where you can expect the above listed typical point accuracy.

## Slide 33: Thanks for your attention
Any question?
For comment/suggestion please send an email to:
support@geomax-positioning.com